## Slide 1
VLIW PROCESSORS

## Slide 2
Introduction:
+ Very Long Instruction Word (VLIW) refers to a processor architecture designed to take advantage of instruction level parallelism.
+ Instruction of a VLIW processor consists of multiple independent operations grouped together.
+ There are multiple independent functional units in VLIW processor architecture.
+ Each operation in the instruction is aligned to a functional unit.
+ All functional units share the use of a common large register file.
+ This type of processor architecture is intended to allow higher performance without the inherent complexity of some other approaches.

## Slide 3
Different approaches
Other approaches to improving performance in processor architectures
+ Pipelining: Breaking up instructions into sub-steps so that instructions can be executed partially.
+ Superscalar architecture: Dispatching individual instructions to be executed completely independently in different parts of the processor.
+ Out-of-order execution: Executing instructions in an order different from the program.

## Slide 4
Instruction Level Parallelism (ILP)
+ Instruction Level Parallelism: is a measure of how many of the operations in a computer program can be performed simultaneously.
+ The overlap among instructions is called instruction level parallelism.
+ Ordinary programs are typically written under a sequential execution model where instructions execute one after the other and in the order specified by the programmer.
+ Goal of compiler and processor designers implementing ILP is to identify and take advantage of as much ILP as possible.

## Slide 5
What is ILP?
Consider the following program:
Op1 e = a + b
Op2 f = c + d
Op3 m = e * f
+ Operation 3 depends on the results of operations 1 and 2, so it can not be calculated until both of them are completed
+ However, operations 1 and 2 do not depend on any other operation, so they can be calculated simultaneously
+ If we can assume that each operation can be completed in one unit of time then these three instructions can be completed in a total of two units of time.
+ Giving an ILP of 3/2
https://www.slideshare.net/shudhanshu29/vliw-processors
http://voer.edu.vn/c/may-tinh-co-lenh-that-dai-vliw-very-long-instruction-word/c046e931/b2fa34fb
https://courses.cs.washington.edu/courses/csep548/06au/lectures/vLIW.pdf
https://researcher.watson.ibm.com/researcher/view_group_subpage.php?id=2833